Login : con0004
15 November 2016
Joaquim Espada
Data transmission

After computing the Hamming Distance between the received message with error 1 the codewords stored in the list of possible messages we can see that the corrected message is “001 111”.
After doing the same to the second message the algorithm wasn't able to correct the error so the message must the retransmitted.

M of N Code

# Introduction

This assignment is carried out within the scope of subject data transmission. In this assignment I will explain the theoretical part of the algorithm M of n Code and also known as Constant Weight Code.
M of n Code is an error detection code algorithm. This kind of algorithm allows the detection of errors in data transmission over unreliable or noisy communication channels. The main idea is that the sender encodes the message in a redundant way by adding a sequence of bits to the original message and the receiver checks the redundant data and determines if has happened an transmission error or not.
In the last part of this assignment will be an implementation of this algorithm using octave programming language.

# M of n Code
The m of n code is a separable error detection code with a code word length of n bits, where each code word contains exactly m instances of a "ones” and also all codewords share the same Hamming weight. This algorithm can't correct errors.
## Hamming Weight
The Hamming weight of a string is the number of symbols that are different from the zero-symbol of the alphabet used.
Example :
Alphabet used	Zero-symbol	String	Hamming Weight
Binary - “1” or “0”	0	11101	4
Binary - “1” or “0”	1	11101000	4
Decimal – “0” until “9”	0	789012340567	10

## Encoding Message
The simplest implementation is to append a string of ones to the original data until it contains m ones, then append zeros to create a code of length n.
Example :
3 of 6 Code
3 → number of “ones” instances
6 → length of the codeword
Original 3 data bits	Appended bits	Encoded Message
000	111	000 111
001	110	001 110
010	110	010 110
100	110	100 110
101	100	101 100
110	100	110 100
111	000	111 000

## Decoding
The easiest way to decode a received message is only to keep the original data bits and discard the appended bits. The size of the original message may be calculated by the following formula:
Original data lenght = n -m
So we should only read the first x bits provided formula and discard the rest.
Note: This algorithm is only valid if the bits are appended in the final of the original message.
Example :
3 of 6 Code
Original data lenght = 6 - 3 = 3
Encoded Message	Discarded Bits	Original 3 data bits
000 111	111	000
001 110	110	001
010 110	110	010
100 110	110	100
101 100	100	101
110 100	100	110
111 000	000	111

## Detecting Error
Regarding the error detection a single bit error will cause the code word to have either m + 1 or m – 1 "ones".

m + 1 case :
Original message : 000 111
Received message : 100 111
Error found!
m - 1 case :
Original message : 000 111
Received message : 000 110
Error found!

Undetected Errors
Original message : 101 100
Received message : 001 101
Observation: If two bits with opposite value are affected by noise and consequently flip their values, this algorithm will not find a the error.
Theoretical Error Correction Algorithm
Has previously stated this algorithm can't correct errors only spot them. So the way that I found to correct the transmission errors is the following the receiver has a list where are stored all possible messages to received. Then is the hamming distance is calculated with the received message and the messages stored in the list. The message stored in the list associated with the computation with the lowest hamming distance value will be the correct message. If more than one computation of hamming distance has the same the message must be retransmitted.
### Theoretical Algorithm Restrain
In this algorithm all the codewords generated by the M of N code must share an minimal Hamming Distance of three to correct one error.
### Hamming Distance
Hamming distance between two strings of equal length is the number of positions at which the corresponding symbols are different.
	000	001	010	011	100	101	110	111
000	0	1	1	2	1	2	2	3
001	1	0	2	1	2	1	3	2
010	1	2	0	1	2	3	1	2
011	2	1	1	0	3	2	2	1
100	1	2	2	3	0	1	1	2
101	2	1	3	2	1	0	2	1
110	2	3	1	2	1	2	0	1
111	3	2	2	1	2	1	1	0

### Codewords for error correction
	000 111	001 110	010 101	011 100	100 011	101 010	110 001	111 000
000 111	0	2	3	4	2	2	4	6
001 110	2	0	4	2	4	2	6	4
010 101	2	4	0	2	4	6	2	3
011 100	4	2	2	0	6	4	3	2
100 011	2	4	4	6	0	2	2	4
101 010	4	2	6	4	2	0	4	2
110 001	4	6	2	4	2	4	0	2
111 000	6	4	4	2	4	2	2	0

Example:
Received Message with error 1: 001 111
Received Message with error 2: 100 001
Codewords	Hamming Distance message 1	Hamming Distance message 2
000 111	1	2
010 101	3	4
011 100	3	6
110 001	5	2
111 000	5	2

## Algorithm Implementation
The algorithm implementation was made using Octave. Octave is a high-level interpreted language, primarily intended for numerical computations. It provides capabilities for the numerical solution of linear and nonlinear problems, and for performing other numerical experiments. It also provides extensive graphics capabilities for data visualization and manipulation. The Octave language is quite similar to Matlab so that most programs are easily portable.
### File run.m
The purpose of the run file is to demonstrate how the algorithm works with several examples.
function run() / m = 3 / n = 6 / printf("Enconding Messages\n") / original_data = [0 0 0; 0 0 1; 0 1 0; 1 0 0; 1 0 1; 1 1 0; 1 1 1] / for i = 1: size(original_data) / temp = original_data(i,:) / encode_message(temp,m,n) / endfor / printf("Decode Messages\n") / original_data = [0 0 0 1 1 1; 0 0 1 1 1 0; 0 1 0 1 1 0; / 1 0 0 1 1 0; 1 0 1 1 0 0; 1 1 0 1 0 0; ] / for i = 1: size(original_data) / temp = original_data(i,:) / decode_message(temp,m,n) / endfor / printf("\n Sending Messages with errors \n") / messages_with_error = [1 0 0 1 1 1; 0 0 1 1 0 0; / 0 0 0 1 1 0; 0 0 0 1 0 0; / 0 0 1 1 1 1; 1 1 1 1 0 1; 1 1 1 0 0 1; / 0 0 0 1 1 1; 1 1 1 0 0 0; 0 0 1 1 1 0] / for i = 1: size(messages_with_error) / temp = messages_with_error(i,:) / error_dectetion(temp,m,n) / endfor / dict = [0 0 0 1 1 1; 0 1 0 1 0 1; 0 1 1 1 0 0;1 1 0 0 0 1; 1 1 1 0 0 0] / message_to_correct = [0 0 1 1 1 1; 1 0 0 0 0 1] / for i = 1: size(message_to_correct) / temp = message_to_correct(i,:) / remove_error(temp,dict) / endfor / endfunction

### File encode_message.m
This file encodes messages accordingly to the Encode Messages section. Dependency on file ones.m.
# message - array with the message / # n - numbers of bits supposed to exist / # m - number of 1 bits supposed to exist / function new_message = encode_message(message,m,n) / n_ones = ones(message) / new_message = [] / #copy original message / for i = 1: length(message) / new_message(i) = message(i) / endfor / # end of copy / counter = length(message)+1 / while(n_ones < m || counter <= n) / if(n_ones < m) / new_message(counter) = 1 / else / new_message(counter) = 0 / endif / counter++ / n_ones++ / endwhile / printf("\nDecoded Message : \n") / decode_message(new_message,m,n) / endfunction

### File decode_message.m
The function on this file decodes messages.
# message - array with the message / # n - numbers of bits supposed to exist / # m - number of 1 bits supposed to exist / function decode_message(message,m,n) / new_message = [] / x = n - m #x = original data size / for i = 1: x / new_message(i) = message(i) / endfor / endfunction

### File ones.m
The function on this file counts the number of ones present in one message. This function is used in the files encode_message.m , error_dectetion.m as an auxiliary function.
function retval = ones(message) / retval = 0 / for i = 1 : length(message) / if(message(i) == 1) / retval++ / endif / endfor / endfunction

### File error_dectetion.m
The function in this file finds errors based in the number of “1” instances regarding the specifications of n and m parameters. Dependency on file ones.m.
# message - array containing the message in binary / # n - numbers of bits suposed to exist / # m - number of 1 bits supposed to exist / function error_dectetion(message,m,n) / n_ones = ones(message) / if(n_ones == m) / printf("\n No error \n") / elseif(n_ones < m) / printf("Case: m - %d \n",(m-n_ones)) / elseif(n_ones > m) / printf("Case: m + %d \n",(n_ones-m)) / endif / printf("\n") / endfunction

### File remove_error.m
Function responsible to remove errors. This function takes as parameters the message to be analyzed for error and the list with code words.
function message = remove_error(m,dict) / c = 20000000000000 / counter = 1 / retransmission_sensor = 0 / message = [] / for i= 1:rows(dict) / dict_temp = dict(i,:) / printf("dict_temp -> %d \n", length(dict_temp)) / temp = hamming_distance(m,dict_temp) / if(temp == c) / printf("\nRestransmission\n") / retransmission_sensor = 1 / break / endif / if(temp < c) / c = temp / message = dict_temp / counter = counter + 1 / endif / endfor / if(retransmission_sensor ==1) / printf("\nRestransmission\n") / else / printf("input message") / m / message / endif / endfunction

### File hamming_distance.m
The function in this file computes the hamming distance between to messages.
# m1 message 1 in binary / # m2 message 2 in binary / # this functions returns the hamming distance value between two / #messages / function d = hamming_distance(m1,m2) / d = 0 / printf("m1 -> %d \n", length(m1)) / printf("m2 -> %d \n", length(m2)) / if(length(m1)==length(m2)) / for i=1:length(m1) / if(m1(i) != m2(i)) / d++ / endif / endfor / else / printf("The messages must have the same lenght \n") / endif / d / endfunction

# Conclusion

After concluding this assignment I concluded that the original M of N Code is can only be used for error detection.
This algorithm can find error by counting the number of ones instances in the message. There are two main cases of error defection, m + 1 case and m – 1. In the first the message has one more instance of one that was supposed to have. In the second case there is a one missing. This error detection algorithm isn't perfect because if two bits are flipped in the message the error will not the found.
Regarding the fact that this algorithm couldn't correct errors I tried develop one. The main idea is that the receiver holds a list where are stored all possible messages to received. Then is computed the hamming distance between the received message and the messages within the list, the message associated with the lowest computation is the correction of the message if there are more than one equal value the message must be retransmitted. The drawbacks of this algorithm is that all codeword must share a minimal hamming distance of three.
About the implementation of the algorithm, the code was written in high-level interpreted language Octave. While coding I had some difficulties because I never had used a mathematical language before, I also used few Octave files with function that allows functions to be reused. In the end I think that code is fairly good and works well.

# References

https://en.wikipedia.org/wiki/Hamming_distance
https://en.wikipedia.org/wiki/Hamming_weight
https://en.wikipedia.org/wiki/Constant-weight_code
https://books.google.de/books?id=8kSjBQAAQBAJ&pg=PA107&dq=m+of+n+code&hl=pt-PT&sa=X&redir_esc=y#v=onepage&q=m%20of%20n%20code&f=false
http://wiki.octave.org/GNU_Octave_Wiki